## Activate SSH :
(config)# ip domain-name laboRT.local
(config)# crypto key generate rsa (Generate RSA key and enable SSH)
(config)# crypto key zeroize rsa (Remove RSA key and disabled SSH)
(config)# username username password password (Create a local user for SSH)
(config)# line vty 0 15 (Select vty 0 to 15)
(config-line)# transport input ssh (Use ssh instead of telnet)
(config-line)# login local (Use local account)
# show ssh (show connected peer)

## Vulnerability:

If Mac table is full, switch enters into fail-open mode. And broadcast all frame to all port. Like a hub.

Send lots of DHCP request to use all ip of the pool address. So DHCP server can't provide any configuration.

Create a fake DHCP server to control DNS resolution and gateway. If you just DoS the main DHCP server you can easily use the technique.

CDP attack: this protocol send all information about a switch to the network. It will be use to auto-configurate some device. But a hack can use this information (take iOS version etc). Or send false information to modify configuration of a device. To disabled CDP: (config)# no cdp run

## Security (way to protect)

### DHCP Snooping:
(config)# ip dhcp snooping (activate DHCP Snooping)
(config)#ip dhcp snooping vlan 10,20 (which port are running DHCP Snooping)
(config-if)# dhcp snooping trust (Where we connect DHCP server),

### Security port:

Static secure MAC addresses: (config-if)# switchport port-security mac-addresse
Add an address in MAC table

Sticky Secure MAC addresses: (config-if)# switchport port-security mac-adresse sticky mac-address
If you tape “(config-if)# switchport port-security mac-adresse sticky” All dynamic MAC address define on this port will be convert into a static configuration and add to the configuration file.

Security violation: ( (config-if)# switchport port-security violation {protect | restrict | shutdown } )
Protected: drop all frame if the MAC source is unknown and the maximum MAC address on this port is reach.
Restrict: Same as Protected but send notification that a security violation has occurred.
Shutdown: (default) shutdown the interface port

Configure NTP (Network Time Protocol):
 (config)# ntp server ip-address (For external NTP server)
(config)# ntp master [stratum] (Define a device as NTP server, client synchronize with the less stratum)