## Activate SSH :
(config)# ip domain-name laboRT.local
(config)# crypto key generate rsa (Generate RSA key and enable SSH)
(config)# crypto key zeroize rsa (Remove RSA key and disabled SSH)
(config)# username username password password (Create a local user for SSH)
(config)# line vty 0 15 (Select vty 0 to 15)
(config-line)# transport input ssh (Use ssh instead of telnet)
(config-line)# login local (Use local account)
# show ssh (show connected peer)

## Vulnerability:

If Mac table is full, switch enters into fail-open mode. And broadcast all frame to all port. Like a hub.

Send lots of DHCP request to use all ip of the pool address. So DHCP server can't provide any configuration.

Create a fake DHCP server to control DNS resolution and gateway. If you just DoS the main DHCP server you can easily use the technique.

CDP attack: this protocol send all information about a switch to the network. It will be use to auto-configurate some device. But a hack can use this information (take iOS version etc). Or send false information to modify configuration of a device. To disabled CDP: (config)# no cdp run

## Security (way to protect)

### DHCP Snooping:
(config)# ip dhcp snooping (activate DHCP Snooping)
(config)#ip dhcp snooping vlan 10,20 (which port are running DHCP Snooping)
(config-if)# dhcp snooping trust (Where we connect DHCP server),

### Security port:

Static secure MAC addresses: (config-if)# switchport port-security mac-addresse
Add an address in MAC table

Sticky Secure MAC addresses: (config-if)# switchport port-security mac-adresse sticky mac-address
If you tape “(config-if)# switchport port-security mac-adresse sticky” All dynamic MAC address define on this port will be convert into a static configuration and add to the configuration file.

Security violation: ( (config-if)# switchport port-security violation {protect | restrict | shutdown } )
Protected: drop all frame if the MAC source is unknown and the maximum MAC address on this port is reach.
Restrict: Same as Protected but send notification that a security violation has occurred.
Shutdown: (default) shutdown the interface port

Configure NTP (Network Time Protocol):
 (config)# ntp server ip-address (For external NTP server)
(config)# ntp master [stratum] (Define a device as NTP server, client synchronize with the less stratum)

# Chapter 3:
Advantages of VLANs:
- Improved Security
- Reduced Cost
- Better Performance
- Smaller Broadcast Domains
- IT Efficiency
- Management Efficiency
Type of VLANs:
- Data VLAN
- Default VLAN
- Native VLAN: use if a non tag frame is receive, so the device tag this frame with the native VLAN (Just for trunk link)
- Management VLAN
You have to use a VLAN just for phone. To define QoS.
Number MAX of VLAN: 4096
When device tag the frame. It add QoS and recalculate FCS.
If the device receive a tagged frame with the same VLAN number as native VLAN, the device drop the frame. So to send control traffic on the native VLAN we have do not tagged the frame.
Normal range VLANs:
1 to 1005. Vlan 1 and 1002 to 1005 is reserved and can't be removed
The database is stored in flash:vlan.dat
Extended VLANs:
Stored in configuration (not in vlan.dat)
## DTP (Dynamic Trunking Protocol):
Disabled DTP: (config-if)# switchport nonegotiate
(config-if)# swichport mode dynamic auto: If it can make an access link
(config-if)# switchport dynamic desirable: If it can make a trunk link (always a trunk except if the other device is configured in access)

# Commands:
# show interfaces f0/1 trunk
# show interfaces fa0/1 switchport