 What bordeless switches have to respect :
Hierarchical - Facilitates understanding the role of each device at every tier, simplifies deployment, operation, and management, and reduces fault domains at every tier
Modularity - Allows seamless network expansion and integrated service enablement on an on-demand basis
Resiliency - Satisfies user expectations for keeping the network always on
Flexibility - Allows intelligent traffic load sharing by using all network resources
Different Switches layers :
- Access Layer : Access layer, wich implement network foundation technologies such as routing, quality of service and security.
  Examples:
  Helps applications to operate on the switched network more safely and securly
  Provides direct, switched network connectivity to the user
- Distribution Layer: Implement:
- Aggregating Layer 2 broadcast domains and Layer 3 routing boundaries
- Providing intelligent switching, routing, and network access policy functions to access the rest of the network
- Providing high availability through redundant distribution layer switches to the end-user and equal cost paths to the core
- Providing differentiated services to various classes of service applications at the edge of network
  Examples:
  Interfaces with the backbone and users to provide intelligent switching, routing and security
  Support Layer 2 broadcast domains and Layer 3 routing boundaries
  Includes redundancy as an important feature for switched network access
  Allow data to flow on equal-cost switching paths to the backbone
- Core Layer: Network backbone with high-speed connectivity. Provide fault isolation.
  Examples:
  The network backbone area for switching
  Can be combined with the Distribution Layer to provide for a collapsed design
  Provides fault isolation and high-speed backbone switch connectivity
It's recommended to make a star network, with Core layer in the middle of all other network.

Definitions:
store-and-forward: Stock the all frame, check the CRC and then send it
cut-throught: forward frame when the switch receives the destination MAC address